## Slide 1
FISHLINIC · CAPSTONE 2026
Smart Aquaculture
powered by AI · Computer Vision · IoT
An autonomous tank that monitors itself, diagnoses fish health,
controls hardware, and explains everything in plain English.
9
MODULES
5
AI MODELS
3
CLIENTS
60s
SCHEDULER TICK
Sejong University · Computer Engineering · 2026
Team Fishlinic — 5 engineers

## Slide 2
THE PROBLEM
Aquaculture is a $300B industry —
still run with thermometers and gut feel.
Manual water testing
Hobbyists test pH, DO₂, temperature 1–2× per week with strips. Fish die from chemistry shifts that happen in hours.
Disease caught too late
Visible symptoms mean disease has spread for days. Without continuous monitoring there is no early warning.
No automation
Feeders run on dumb timers. Lights ignore sensors. Pump on/off is manual. The system can't react to its own state.
→ We built the system that does all three. Continuously. Autonomously. Explainably.

## Slide 3
THE SOLUTION
Fishlinic — one connected stack from sensor to AI
SENSE
Arduino sensors stream pH, temperature, dissolved O₂, CO₂ at 1 Hz over USB serial. Mock mode keeps demos working without hardware.
REASON
Veronica — local LLM agent (Ollama + qwen2.5:3b) with tool-calling. Reads sensors, controls hardware, explains decisions.
SEE
YOLOv11 disease detector + counting model + ConvLSTM-VAE behavior anomaly detector run continuously on the camera feed.
ACT
Relay-driven feeder, air pump, LED strip. Cron-style scheduler orchestrates feed times, lighting cycles, and emergency overrides.
All four pillars feed each other. Reason → Act loop closes the system.

## Slide 4
ARCHITECTURE
Five services. One source of truth.
Arduino · Main
pH · DO₂ · CO₂
Arduino · Secondary
Temp · Relays
USB Camera
1080p · YOLO feed
Hardware actuators
Feeder · Pump · LED
Serial Bridge :3001 (Node.js)
USB JSON → REST · MOCK_MODE fallback
AI Predictor :8001 (FastAPI)
YOLOv11 · ConvLSTM-VAE · Random Forest
NestJS Backend · :3000
9 modules: sensors · alerts · actuators · vision · voice · fish · cron · gateway · management
REST + Socket.IO · TypeORM (SQLite/Postgres) · Cron tick @60s
Mobile App
Expo SDK 54 · iOS / Android / Web
Dashboard
Next.js 16 · React 19 · NextAuth
Veronica LLM
Ollama :11434 · qwen2.5:3b
Slide 4 of 16 · Architecture

## Slide 5
TECH STACK
Production-grade tooling, end to end.
Backend
NestJS · TypeScript
TypeORM · Socket.IO
Class-validator
Mobile
Expo SDK 54 · RN 0.81
React 19 · React Native
Keyboard Controller
Dashboard
Next.js 16 · React 19
Tailwind · NextAuth
Server Components
AI Pipeline
FastAPI · PyTorch
Ultralytics · scikit-learn
OpenCV
LLM Agent
Ollama · qwen2.5:3b
Tool-calling protocol
Local inference
Storage
PostgreSQL (prod)
SQLite (dev)
better-sqlite3 driver
Monorepo: pnpm workspaces · 3 apps + 3 services + shared types · 50k+ LOC TypeScript

## Slide 6
FLAGSHIP FEATURE
Meet Veronica —
the AI agent that actually runs the tank.
Local LLM
Runs entirely on-device via Ollama. No cloud, no API fees, no privacy concerns.
Tool-calling
Reads sensors, controls hardware, queries history. 6 tools wired into the agent loop.
Confirm-before-act
User mode requires confirmation. Auto mode lets Veronica respond to emergencies alone.
Sessioned chat
Persists every conversation. Restores context across app reopens.
Veronica · LIVE
How are my fish today?
pH 7.1, temp 26°C, DO 7.4 mg/L — all healthy. Vision detected 12 active fish, no stress signs. Last feeding 3h ago.
Turn on the LED.
⚡ ACTION: Turn LED ON. [Cancel] [Confirm]

## Slide 7
COMPUTER VISION
Three models. One camera feed.
YOLOv11 · DISEASE
yolo_disease.pt
Trained on a curated set of fungal infection, fin rot, ich, and ulcer images. Runs every camera tick when fish are visible. Bounding boxes + confidence per disease class.
8 classes
PATHOLOGIES
YOLOv11 · COUNT
yolo_count.pt
Counts active fish per frame. Drives the population badge in the UI and detects population drops that may indicate mortality events.
± 1 fish
ACCURACY
ConvLSTM-VAE
convlstm_vae.pth
Variational autoencoder over 5-frame sequences. Learns 'normal' fish swimming patterns. High reconstruction loss → behavior anomaly (stress, hypoxia, panic).
5 frames
TEMPORAL WINDOW
Inference runs in FastAPI service on port 8001 — auto-detects GPU/CPU, batches frames

## Slide 8
REAL-TIME PIPELINE
From Arduino to your phone in 200 ms.
Chart: Live sensor stream — last 5 min
| t-5m | t-4m | t-3m | t-2m | t-1m | now
pH | 7.1 | 7 | 7.2 | 7.1 | 7 | 7.1
Temp °C | 25.4 | 25.6 | 25.8 | 26 | 26.1 | 26
DO mg/L | 7.5 | 7.4 | 7.4 | 7.3 | 7.4 | 7.5
01
Arduino sample
10 ms
ADC reading + JSON encode
02
USB serial → Bridge
30 ms
9600 baud · packet validate
03
REST → Backend
20 ms
POST /serial/reading · TypeORM persist
04
Socket broadcast
5 ms
sensor:update event to all clients
05
Client UI render
16 ms
React state update · 60fps animation

## Slide 9
MOBILE
Cross-platform native UI — built once, runs everywhere.
Live Sensors
Real-time pH, temp, DO gauges with smooth animations.
Tank Controls
Manual feed trigger, pump and LED toggles, schedule editor.
Veronica Chat
Voice + text interface to the AI agent with session history.
Fish Health
Live disease detection feed with confidence scores and trend.
Push Alerts
Critical thresholds trigger real device push notifications.
Expo SDK 54 · React Native 0.81.5 · React 19 · Keyboard Controller · AsyncStorage · expo-speech · expo-notifications

## Slide 10
WEB DASHBOARD
Mission control for your aquaculture operation.
fishlinic.dashboard / live
Fishlinic Monitor · Tank #1
pH
7.1
OK
TEMP
26°
OK
DO
7.4
OK
FISH
12
ACTIVE
LIVE TELEMETRY · 24h
Chart: 
| 00 | 04 | 08 | 12 | 16 | 20 | 24
pH | 7.1 | 7 | 7 | 7.2 | 7.1 | 7 | 7.1
⚠ Cleaning reminder · last cleaned 14 days ago
Live telemetry charts
One-click hardware controls
Camera feed with detections
Embedded Veronica chat
NextAuth — Google + email
Team profiles + roles

## Slide 11
ENGINEERING HIGHLIGHTS
The non-obvious decisions that made it work.
60-second cron tick
Single timer drives all scheduled work — no fragile multiple cron jobs. Feeders, lights, cleaning, alerts all on one beat.
Mock mode everywhere
Backend + bridge fall back to simulated data when hardware is offline. Demos work without an Arduino plugged in.
Bidirectional sockets
Server emits telemetry; clients emit commands. Single Socket.IO gateway handles both directions with type-safe events.
Tool-calling agent
Veronica uses Ollama function-calling to read sensors and act. Agent loop with iteration limit + confirmation gating prevents runaway.
Atomic Design
Atoms → molecules → organisms → screens. Mobile and dashboard share the same component vocabulary across teams.
Shared TypeScript
All services + apps import types from shared/types. One change to a sensor type ripples to mobile, dashboard, backend instantly.

## Slide 12
BY THE NUMBERS
Six months of work, shipped.
50K+
Lines of TypeScript
Backend, mobile, dashboard, shared
9
Backend modules
sensors · alerts · actuators · vision · voice · fish · cron · gateway · management
5
AI models
YOLOv11×2, ConvLSTM-VAE, RF, Qwen2.5
3
Client surfaces
Mobile (iOS/Android/Web), Dashboard, Voice
200ms
Sensor → UI latency
Arduino → Bridge → API → Socket → Phone
100%
Offline-capable
Local LLM + mock mode + local DB

## Slide 13
LIVE DEMO
How it all comes together — one minute, end to end.
0:00
Tank state
Open dashboard. Live pH 7.1, temp 26°C, 12 fish counted by YOLO.
0:15
Manual feed
Tap 'Feed' on mobile. Relay clicks. Camera shows fish swarming.
0:25
Disease detected
YOLO flags possible fin rot — alert pops up on mobile + dashboard.
0:40
Ask Veronica
Voice query: 'how are my fish today?' She reads sensors + diagnoses live.
0:55
Autonomous action
Switch to auto mode — Veronica sees high temp, turns on pump unprompted.

## Slide 14
THE TEAM
Five engineers. Five disciplines. One product.
Ismail
Lead Architect
Backend (NestJS), Mobile (Expo), Veronica agent, system integration
Maral
Database Specialist
TypeORM schemas, migrations, Supabase production wiring
Hamidullah
Frontend Engineer
Dashboard, atomic UI system, mobile styling polish
Firdavs
AI Engineer
YOLOv11 disease + count, ConvLSTM-VAE, Random Forest pipeline
Sarvar
Hardware Engineer
Arduino firmware (main + secondary), USB serial protocol, relays
Sejong University · Computer Engineering Department · Capstone 2026

## Slide 15
WHAT'S NEXT
From capstone to product.
PHASE 1
Production Hardening
Q3 2026
Multi-tank scaling (1 backend, N tanks)
TimescaleDB for sensor history
AWS / GCP deployment with Terraform
OAuth role-based access (owner/staff)
PHASE 2
Smarter AI
Q4 2026
Quantize Veronica to 4-bit (Q4_K_M)
Fine-tune on aquarium-specific corpus
Vision-language model for camera Q&A
Predictive maintenance from sensor trends
PHASE 3
Commercial Pilot
Q1 2027
Partnership with local fish farms
Subscription tier with cloud sync
Industrial-grade sensor packages
Mobile-first marketplace for replacements

## Slide 16
Thank you.
Built with obsession for the fish. 🐟
FISHLINIC
Smart Aquaculture System · Sejong University Capstone 2026
github.com/Ismoiljon1101/capstone_aquarium_sejong
Questions?